In hand placing the poles, we used the place() function in Octave. We did this in a Jupyter Lab IPython Notebook with the Octave kernel. We set tried setting different poles to find the gain values that worked the best for our system. With poles = [-10 -5] (first value for position and second for angular velocity), we achieved the best gain with gain = [0.1720 0.1129] .
From our thrust modeling we found that the hover copter balances when the motor is producing about 40 grams of thrust which corresponds to a PWM value of about 80 which we set as our large signal PWM. Our small signal PWM is given by -G·X·1023 where G is our 1x2 gain matrix and is our 2x1 state variable matrix. The purpose of the 1023 multiplication is to scale the gain values over the possible range of PWM values. The small signal is added to the large signal PWM after each read of the rotary angle encoder